## Slide 1
LightTrap Simulation — Analysis Summary
Two-layer WLS light trap · Geant4 optical photon transport
Run: output_apexltsim0.root · 10,000,000 primary photons
Source: analysis/analyze_lighttrap.ipynb (PyROOT + RDataFrame)

## Slide 2
OVERVIEW
Device & simulation data model
• Two-layer light trap converts UV → blue, guides light to edge SiPMs
  – First layer: thin pTP film on UV-transparent acrylic carrier — absorbs incident UV, re-emits near-UV/blue
  – Second layer: blue-WLS acrylic slab — re-emits blue, transports by TIR
  – SiPMs sit flush to the ±y edges of the slab; Vikuiti ESR foil backs it
  – 15 cm × 15 cm module; pTP 2 µm / UV-acrylic 3 mm / LAr gap 3 mm / blue slab 6 mm
• 9 TTrees record every stage of the photon chain
  – Primary, WLSPhoton (births), SiPMPhotons/SiPMHits (pre/post-PDE)
  – Leak counters: FirstLayerBackplane / FirstLayerEdges / SecondLayerBackplane
  – OpticalValidation: Fresnel refl/ transmit at first surface
10.0 M
primary photons
14.1 M
WLS births
558 k
reach SiPM
333 k
detected p.e.

## Slide 3
KEY RESULT
Efficiency chain
85.90%
pTP WLS eff. (N_pTP / N_primary)
10.06%
collection (SiPM / blue)
6.01%
detection (hits / blue)
3.34%
overall (p.e. / primary)

## Slide 4
SPECTRA
Wavelength spectra — the WLS cascade
• Each stage shifts redward
  – Incident primary UV is absorbed by pTP
  – pTP re-emits in the near-UV/blue
  – Blue-WLS slab re-emits deeper blue
  – Spectrum arriving at SiPM matches the blue-WLS emission, folded with transport
• Confirms the two-stage down-conversion works as designed

## Slide 5
GEOMETRY CHECK
SiPM spatial hit maps
• Two bands at y ≈ ±75 mm
  – Confirms SiPMs on the ±y slab edges
  – Pre-PDE vs post-PDE shows detection thinning (≈60% PDE)
  – z-profile clusters at the blue-slab depth
• 558 k reach SiPM → 333 k detected

## Slide 6
DIAGNOSTICS
Angular & timing distributions
WLS emission cos θ and φ (isotropy check) · photon arrival time at the SiPMs
• cos θ and φ are flat → isotropic re-emission for both pTP and blue emitters; arrival-time spread reflects TIR path-length variation

## Slide 7
LOSS ANALYSIS
Photon fate budget & leak accounting
• Where first-layer light goes
  – 8.59 M pTP births
  – 11.3 M cross the 1st back face into the gap
  – 270 k escape laterally at ±x edges (loss)
  – 5.55 M blue-WLS births downstream
  – Only 433 leak through the 2nd backplane (Vikuiti works)
• Dominant loss is optical transport, not backplane leakage

## Slide 8
SANITY CHECK
Optical validation — Fresnel reflectance
• Reflected fraction rises with incident angle
  – Expected Fresnel behaviour at the first surface
  – 4.53% of 10 M primaries reflected overall
  – 95.47% transmitted into the stack
• Confirms surface optics are modelled correctly

## Slide 9
TAKEAWAYS
Summary & conclusions
85.90%
pTP WLS efficiency
64.59%
2nd-stage conversion
10.06%
collection to SiPM
59.76%
average PDE
3.34%
detected photoelectrons per incident primary
• pTP first-layer conversion is highly efficient (86%)
• End-to-end yield is transport-limited: collection to the SiPMs is the bottleneck (~10%)
• Backplane leakage is negligible (433 of millions) — Vikuiti foil performs
• Lateral ±x edge escape (270 k) is a recoverable loss channel
• Reproducible: re-point ROOT_FILE in the notebook to analyze any run

## Slide 10
The new scripts run the simulation with and without PTFE or Vikuiti foils at the backplane.
An analysis script comparing those results needs to be written.